## Slide 1: SURVEY SAYS: ALTA SURVEYS, SURVEY EXTENDED COVERAGE, AND RELATED ENDORSEMENTS
Presented by:
Brady McGarry, Professional Land Surveyor, Chase Jones & Associates and
Justin Carter, Underwriting Counsel, Chicago Title and Ticor Title

## Slide 2: Presentation Roadmap
When is a survey required?
The Mechanics of Survey Coverage
What is an ALTA/NSPS Survey?
  Minimum Standards
  Table A Optional Items
Discussion of Related Endorsements and Table A Items

## Slide 3: When do I need a Survey?
Variations per underwriter
Always: Owner’s Extended Policies
Generally: Lender’s Extended Policies insuring $1,000,000 or more
  Exceptions on a case by case basis
  No exceptions for farm and ranch land
  Typically, no exceptions for new construction
Several Endorsements (maybe):
  Covenants, Conditions, Restrictions, Private Rights, Minerals – 209 series
  Contiguity - 219s
  Access - 217s
  Same as Survey - 225 (it has survey in the title)

## Slide 4: Mechanics
The survey related exceptions, which are standard exceptions 2-4, are replaced by a specific exception for matters disclosed by the survey.
Standard Exceptions
  2. Any facts, rights, interests or claims, which are not shown by the Public Records but which could be ascertained by an inspection of the Land or which may be asserted by persons in possession thereof.
  3. Easement, or claims thereof, which are not shown by the Public Records; reservations or exceptions in patents or in Acts authorizing the issuance thereof; water rights, claims or title to water.
  4. Any encroachment, encumbrance, violation, variation, or adverse circumstance affecting the Title that would be disclosed by an accurate and complete land survey of the Land.
Replaced by New Exceptions: “Any rights, interest, or claims which may exist or arise by reason of matters disclosed by that ALTA/NSPS Land Title Survey last dated June 24, 2016 by Guy Surveyor, of Surveyor & Associates, P.S. for: (a) storm drain lines connecting to the adjacent Texaco parcel; (b) building line encroaching over the northerly 1.2 feet.”

## Slide 5: Mechanics Continued – Policy boilerplate
Covered Risk 2(c) ALTA Owner’s and Loan Policies – A defect in the Title caused by –
2021 Form
2006 Form
Comments

## Slide 6: What is an ALTA/NSPS survey?
Meets the minimum standards promulgated by the American Land Title Association and the National Society of Professional Surveyors (formerly the American Congress of Surveying and Mapping)
Minimum Standards Include
  Boundary lines
  Building footprint
  Location of utilities
  Location of recorded easements
  Evidence of unrecorded rights
Additional Items

## Slide 7: ALTA/NSPS Standards
Most recent promulgation: 2021
Minimum Standards
  Fieldwork must meet certain technical measurement standards of precision. 3(E).
  Depict
    monuments found and set (if required) and boundary lines. 5(A)(i-iii).
    adjoining streets, access to a public rights of way, and potential unrecorded rights. 5(B)(ii-v).
    evidence of possession, significant improvements within 5 ft. of boundary lines, and potential encroachments into easements or setbacks disclosed in documents, 5(C), and buildings, 5(D).

## Slide 8
Example Survey Issue: Locating fence corner

## Slide 10: ALTA/NSPS Standards
Most recent promulgation: 2021
Minimum Standards
  Fieldwork must meet certain technical measurement standards of precision. 3(E).
  Depict
    monuments found and set (if required) and boundary lines. 5(A)(i-iii).
    adjoining streets, access to a public rights of way, and potential unrecorded rights. 5(B)(ii-v).
    evidence of possession, significant improvements within 5 ft. of boundary lines, and potential encroachments into easements or setbacks disclosed in documents, 5(C), and buildings, 5(D).
    recorded easements and potential unrecorded easements including utilities and utility locate markings. 5(E)(i-ii).
    surface evidence of utilities including utility locate markings, and also utility poles within 10 ft. of boundary lines. 5(E)(iii-iv).
    boundary lines with labeled courses, point of beginning, and point of commencement if applicable. 6(B)(iii).
    any lack of contiguity (gaps, gores, and overlaps) between the subject property and adjoiners. 6(B)(vii).
    building locations labelled perpendicular to property lines. 6(B)(ix).
    locations of plottable easements. 6(C)(i).
  North arrow, legend, and certification to the insured (buyer/borrower), title company, and the lender. 6(D) & 7.
Optional Table A Items – often required for specific endorsements

## Slide 11: Table A
Table A is essentially a request to the surveyor to include certain Items on the survey
Requests are communicated by the customer checking Items on Table A
Some Items are dictated by lender requirements and others by title insurance requirements
Title insurance requirements correlate with specific endorsements

## Slide 12: Table A Commonly Requested Items

## Slide 13: Table A Commonly Requested Items

## Slide 14: Endorsements and ALTA Surveys
Endorsements that will be covered
  Zoning Endorsements – OTIRO 203s
  Covenants, Conditions, Private Rights, Encroachments - OTIRO 209 series
  Access Endorsements – OTIRO 217s
  Contiguity Endorsements – OTIRO 219s
  Same as Survey Endorsements – OTIRO 225s
  Encroachment Endorsements – OTIRO 228s
Table A Items that will be covered
  Substantial features observed in the process of conducting fieldwork in addition to those required in Sec. 5. Item 8.
  List zoning requirements supplied to the surveyor, Item 6(a), and depict setbacks, if no interpretation required by the surveyor, Item 6(b).
  Dimensions, square footage, and height of buildings. Item 7(a) - (c).
  Parking spaces. Item 9.
  Appurtenant easements. Item 18.
  Location of utilities on or serving the property as determined by plans or locate markings. Item 11.
Also several minimum standards will be covered

## Slide 15: 209 Series and Encroachment Endorsements
Minimum Standards
  boundary lines. 5(A)(iii).
  potential unrecorded rights. 5(B)(v).
  evidence of possession, significant improvements within 5 ft. of boundary lines, buildings, and potential encroachments into easements or setbacks disclosed in documents, 5(C), and buildings 5(D).
  recorded easements and potential unrecorded easements including utilities and utility locate markings. 5(E)(i-ii).
  surface evidence of utilities including utility locate markings and also utility poles within 10 ft. of boundary lines. 5(E)(iii-iv).
  boundary lines with labeled courses, point of beginning, and point of commencement if applicable. 6(B)(iii).
  building locations labelled perpendicular to property lines. 6(B)(ix).
  locations of plottable easements. 6(C)(i).
Table A Items
  Substantial features observed in the process of conducting fieldwork in addition to those required in Sec. 5. Item 8.

## Slide 16: ALTA Survey – without Table A Items

## Slide 17: ALTA Survey with “Normal” Table A Items

## Slide 18: OTIRO 209 Series
Disclaimer—this is a very broad summary of the 209 series
Generally, insures against loss or damage caused by violations of covenants, conditions, and restrictions unless exception is taken in policy.
Varying definitions of improvement.
  Eg. 209.2-06—a building, structure located on the surface of the Land, road, walkway, driveway . . . That by law constitutes real property but excluding crops, lawn, shrubbery, or trees.
  Eg. 209.3-06—includes lawn shrubbery, or trees affixed to the Land at Date of Policy.
If the endorsement covers damage to future improvements, we require a site plan of the contemplated development.
Note—Not all violations of covenants are survey matters
  Eg. Use violations or style and design violations
Note—Some endorsements in the 209 series also offer coverage for matters that are strictly title, not survey
  Eg. exercise of an option to purchase, right of first refusal, or right of prior approval
  Eg. damage caused by exercise of surface mineral extraction rights

## Slide 19: Encroachment Endorsements
Endorsement 228-06 Easement Damage or Forced Removal –
  Insures against loss caused by damage to a building or enforced removal of an improvement because of an encroachment in the enumerated easement
Endorsement 228.1-06 and 228.1 Encroachments Boundaries & Easements –
  Insures against loss caused by encroachments of improvements on or off the land or into easements
  Improvements = existing buildings
Endorsement 228.2-06 Encroachment Boundaries and Easements, Described Improvements
  Insures against loss caused by encroachments of improvements on or off the land or into easements
  Improvements = what we define as improvement in the endorsement
Endorsement 228.3-06 Encroachments Boundaries & Easements Land Under Development –
  Insures against loss caused by encroachments of current or future improvements on or off the land or into easements
  Improvements = more broadly defined. Includes building, structure, or paved area.
  We require an ALTA survey and site plans.

## Slide 20: Zoning Endorsements – 203s
Minimum Standards
  Location of buildings 5(D) and building locations labelled perpendicular to property lines. 6(B)(ix).
Table A Items that may be necessary
  List zoning requirements supplied to the surveyor, Item 6(a), and depict setbacks, if no interpretation required by the surveyor, Item 6(b).
  Dimensions, square footage, and height of buildings. Item 7(a) - (c).
  Parking spaces. Item 9.
  Gross land area. Item 4.

## Slide 21: Table A – Item 6(a) & (b)
Note for 6(a)
On map for 6(b)

## Slide 22: Table A - Item 7
With Item 7(a), 7(b)(1), & 7(c)
Without Item 7(a), 7(b)(1), & 7(c)

## Slide 23: Table A - Item 9
Shown on map
Noted on map

## Slide 24: Zoning Endorsements
Endorsement 203-06 Zoning Unimproved Land and 203 Zoning –
  Insures against loss caused by failing to report the correct zoning classification and allowed uses.
  Typical requirements are a letter from the appropriate government authority or zoning report that
    states the zoning classification for this property and
    the types of uses that are permitted in under this classification

## Slide 25: Zoning Endorsements
Endorsement 203.1-06 Zoning Improved Land and 203.1 Zoning Completed Structure –
  Insures against loss caused by failing to report the correct zoning classification and allowed uses.
  Typical requirements are a letter from the appropriate government authority or zoning report that
    states the zoning classification for this property and
    the types of uses that are permitted in under this classification
  Additional requirements include checking that the items listed in paragraph 2 of the 203.1-06 or paragraph 3 of the 203.1 of the endorsement comply with the current zoning classification.

## Slide 26: Zoning Endorsements
Endorsement 203.1-06 Paragraph 2
2. The Company further insures against loss or damage sustained by the Insured by reason of a final decree of a court of competent jurisdiction . . . requiring the removal or alteration of the structure, because, at Date of Policy, the zoning ordinances and amendments have been violated with respect to any of the following matters:
  a. Area, width, or depth of the Land as a building site for the structure
  b. Floor space area of the structure
  c. Setback of the structure from the property lines of the Land
  d. Height of the structure, or
  e. Number of parking spaces.
Similar but not identical to 203.1 paragraph 3

## Slide 27: Zoning Endorsements
Endorsement 203.2-06 and 203.2 Zoning Land Under Development –
  Insures against loss caused by failing to report the correct zoning classification and allowed uses.
  Typical requirements are a letter from the appropriate government authority or zoning report that
    states the zoning classification for this property and
    the types of uses that are permitted in under this classification
  Additional requirements include checking that the items listed in paragraph 3 of the endorsement comply with the current zoning classification and
  Checking that the items listed in paragraph 3 of the endorsement comply with the site plan for the proposed building

## Slide 28: Access Endorsements
Minimum Standards
  adjoining streets and access to a public rights of way. 5(B)(ii-iv).
  any lack of contiguity (gaps, gores, and overlaps) between the subject property and adjoiners. 6(B)(vii).
  surface evidence of utilities including utility locate markings and also utility poles within 10 ft. of boundary lines. 5(E)(iii-iv). (Sort of)
Table A Items
  Appurtenant easements. Item 18.
  Location of utilities on or serving the property as determined by plans or locate markings. Item 11.

## Slide 29: Survey Access and Contiguity Issue

## Slide 30
Plat was done in 1988.
Survey Issue

## Slide 31
City monumented the Street in 1992.
Survey Issue

## Slide 32
Detail on ALTA/NSPS Land Title Survey.
Survey Issue

## Slide 33: Access Endorsements
Endorsement 217-06 Access and Entry –
  Insures that the property abuts a publically dedicated, open road, with no obstructions or obstacles to access (cub cuts in place, no gaps).
  Two elements of coverage –
    Legal access from abutting a publically dedicated right of way
    Physical access without obstruction
Compare to Covered Risk 4
  Owner’s and Loan Policy Covered Risk 4  Policy insures against loss or damage sustained by
    “No right of access to and from the Land.” (Same for both 2006 and 2021 form policies)
  Differences – I see two
    Policy access does not specify source of legal access
    Policy access does insure physical access

## Slide 34: Survey Access Issue

## Slide 35: Access Endorsements
Endorsement 217.1-06 Indirect Access and Entry–
  Insures that an appurtenant access easement commences on a publically dedicated, open road, and terminates on the boundary of the insured property, with no obstructions or obstacles to access (curb cuts in place, no gaps – consult survey).
  The form of this endorsement requires that the appurtenant easement be a separate parcel.
  Often require an ALTA Survey that includes the appurtenant easement.

## Slide 36: Access Endorsements
Endorsement 217.2-06 Utility Access
  Insures that specified utility types have legal access to the property
  Often require an affidavit by the seller that specific utilities serve the property
  May also require an ALTA survey to show no gaps, gores, or overlaps between the subject property and adjoining properties or streets and depicting utility lines that service the property.

## Slide 37: Contiguity Endorsements – three types
Minimum Survey Standard
  any lack of contiguity (gaps, gores, and overlaps) between the subject property and adjoiners. 6(B)(vii).
Endorsement 219-06 Contiguity Multiple Parcels –
  Insures that that all of the parcels in the policy about each other in some combination without gaps or overlaps.
Endorsement 219.1-06 Contiguity Single Parcel –
  Insures that the property abuts its neighbors on all sides without gaps or overlaps.
Endorsement 219.2-06 Contiguity Specified Parcels –
  Insures that there are not gaps, gores, or overlaps between the specified parcels.

## Slide 38: Same as Survey Endorsements
Minimum Survey Standard
  boundary lines with labeled courses, point of beginning and point of commencement if applicable. 6(A), (B)(iii).
Endorsement 225-06 Same as Survey –
  Insures that the survey depiction and the policy description describe the same property
Endorsement 225.1-06 – Same as Portion of Survey Endorsement –
  Insures that the survey depiction and the policy description describe the same property for the specified parcels

## Slide 39
Thank you!!
Questions?
Feel free to call with additional questions:
Justin Carter, Underwriting Counsel,
Chicago Title Insurance Company,
justin.carter@ctt.com, 503-250-4554
Brady McGarry, Professional Land Surveyor,
Chase Jones & Associates,
brady@chasejonesinc.com, 503-228-9844